## Slide 1: 2050 Calculator

## Slide 2: Implementation
Model excel file
Convert / compile C
Server host model

## Slide 3
Input
User input
Hard-coded data / coefficients
Model
Calculate
Web
Energy Stacked bar chart
Land use
Greenhouse gas emission
Cost
Energy demand/supply
Bar charts
Flow chart

## Slide 4: Model Description

## Slide 5: User Input
`Trajectory’ values for supply / demand (ranging 1-4)
  Example:
    Nuclear power generation
      1: No new nuclear
      2: 13 3GW power stations (by 2050)
      3: 30 3GW power stations (by 2050)
      4: 50 3GW power stations (by 2050)
    Average temperature of homes
      1: 20’C (high)
      2: 18’C
      3: 17’C
      4: 16’C (low)
These values are `preset’ by the developers (make it easier for people)
Goals are interpolated linearly, from present time to 2050.

## Slide 6: Cost calculation
Cost per unit generation (there is a projected cost curve)
  For example:
    Fossil fuel prices set at $130/barrel (large overestimation, I think)
    Solar PV costs decrease with time
Discount rate (default 3.5%)
Three calculations for cost:
  Best, point, worst
  Provides range of cost calculations

## Slide 7: Data / assumptions
Purple-colored sheets have the assumptions / data that pertain to the rates / coefficients
  Conversions
    Unit conversions
    Currency conversions
    Deflation of GDP
  Global assumptions
    Population projection
    GDP projection
    Discounting
    Financing costs
  Constants
    Calorific values from fuels (TWh/kg or TWh/m3 or TWh/l)
    Combustion emissions factor
    Global warming potential

## Slide 8: Hard-coded variables
18 `sectors’ for energy generation and consumption
  Trajectory choices and values
  Fixed assumptions
    Cost assumptions
    Efficiency
    Load factors
    Emission factors
    Etc.

## Slide 9: Output Values
Energy supply / demand
  Different sectors
Greenhouse gas emissions
Security
  Energy imports
Land use
Costs

## Slide 10: U.S. version plans

## Slide 11: Quick method
Change / revaluate data:
  Conversions
    Currency conversions
    Deflation of GDP
  Global assumptions
    Population projection
    GDP projection
    Discounting
    Financing costs
  Constants
    Calorific values from fuels (TWh/kg or TWh/m3 or TWh/l)
    Combustion emissions factor
    Global warming potential
  18 sectors’ coefficients

## Slide 12: Longer / complex method
Quick method + redesign to make more transparent
  Instead of an excel file -> C -> web,
  Python module with an external database (e.g. HDF5) for assumptions / data
    Which can be updated from a reputable source
      For example:
        uranium / oil prices linked to commodities market database
        Currency linked to currency market
        Interest rate linked to bond rates

## Slide 13: Estimated time of implementation
Quick method
  A great summer (graduate) intern
  With guidance
Longer method
  2-3 months of full time work